## Slide 1: PSS Operation Models
Hands-on: one device model → SystemVerilog, C, C++, Python
Matthew Ballance
Notes: Diagrams are native shapes generated from diagrams/make_diagrams.py. Labs: labs/lab1, labs/lab2 (see labs/README.md).

## Slide 2: Agenda
1
Intro: what and why
Integration, drift, and how far PSS gets us today
2
Operation-model anatomy
What an operation model has to provide, and how it maps to SV and C
3
Lab 1: Core structure
Component tree, initialization, export and import functions; generate and integrate
4
Lab 2: Registers and memory
Register models from SystemRDL; programming sequences

## Slide 3: Intro: what and why
Integration and the need for consistent content

## Slide 4: Challenge 1: integration needs content
SoC
CPU core
Interconnect
DMA
Comm ctrl (UART/SPI)
Timer
Memory ctrl
each block: complex to configure and operate,
alone and in combination
SoC DV
SystemVerilog / UVM
Emulation
C on core + SV
Firmware
C, bare-metal
Post-silicon
C / Python, lab
every team programs every block
Notes: Systems are composed of many design blocks: processor core, interconnect, comm controller. Each needs complex programming to configure and operate, individually and in aggregate. Most apparent on integration teams: SoC, emulation, firmware, post-silicon.

## Slide 5: Challenge 2: drift
DMA
one device
SoC DV
CSR.en = 1
SZ = 64
poll CSR.done
Emulation
SZ = 64
CSR.en = 1
poll CSR.done
≠ order
Firmware
CSR = 0x1 // prio=0!
SZ = 64
wait IRQ
≠ prio lost
Post-silicon
SZ = 0x40
CSR.en = 1
sleep(1ms)
≠ no completion check
4 teams → 4 sequences
→ 4 different behaviors
“Works in sim, fails on the board”
Notes: One team tests one way, another differently. One small config/programming difference causes the device to behave very differently. Major cause of integration headaches.

## Slide 6: Bottom line: one device, four delivery requirements
We need consistent device-programming content, delivered in several languages and methodologies.
Team | Language | What it needs
SoC DV | SystemVerilog / UVM | time-consuming tasks, sequencer-driven bus access
Emulation | C on the core, SV on the host | small footprint, fast
Firmware | C, bare-metal | no heap, no scheduler, volatile MMIO
Post-silicon | C / Python | scripting, lab debug, real hardware
Same device knowledge, four different delivery requirements.

## Slide 7: PSS: the visible solution for portable tests
PSS test description
dma_xfer_a
rand size, chan
CSR, SZ, SRC, DST
uart_tx_a
rand baud, len
LCR, DLL, THR
tmr_wait_a
rand ticks
LOAD, CTRL, STS
decisions (random) + register programming
generator
SV / UVM test
C test on the core
C test in the lab
…
Notes: PSS test description -> generator -> test implemented in one of many languages. Each action bubble carries randomization AND register programming.

## Slide 8: Two key pieces in every action
One action, two very different jobs
Scenario (decide)
• what to do, in what order
• random choices under constraints
• resources, data flow, scheduling
test-specific; changes per test
Realization (do)
• how to make the device do it
• register/memory programming
• waiting for completion, errors
device-specific; same for everyone
calls
Scenario / decision and realization (device driver, device utility).

## Slide 9: PSS elements, briefly
Component tree
structure
component pss_top {
dma_c dma;
uart_c uart[2];
timer_c tmr;
}
provides structure: instances,
resources, register banks
Actions
scenario: flow + choices
action dma_xfer_a {
input buf_s src;
output buf_s dst;
lock chan_r ch;
rand bit[16] size;
}
data-flow + resource relationships;
make the random choices
Procedural code
realization
exec body {
comp.regs.sz.write_val(size);
comp.regs.csr
.write_field("en", 1);
plat_wait_irq();
}
carries out decisions: calls
functions, touches registers

## Slide 10: What is a test?
Limited parameterization
A seed and a few knobs, not an API
Autonomous
Exercises the design within the given parameters and checks as it goes
Clear pass/fail
One verdict at the end
A test is one consumer of device knowledge, and not the most common one.

## Slide 11: PSS adoption: requirements vs. reality
Who needs device-programming content?
PSS tests
UVM sequences
firmware / drivers
emulation bring-up
lab scripts
where PSS adoption
usually stops
need the same device knowledge — but aren’t “tests”
Adopting PSS for tests requires…
• PSS as the test-description language
• PSS content for every device a test touches
• …and actually writing tests
…but in practice
• mission-mode firmware exercises the design — not a test
• teams can’t (yet) write full tests in PSS
• PSS doesn’t exist for every device

## Slide 12: Taking PSS beyond test reuse
Separate realization from scenario. At this point it's a simple separation:
Before: one action does both
After: realization moves to the component
action xfer_a {
rand bit[16] size;
constraint size in [1..4096];
exec body {
comp.regs.sz.write_val(size);
comp.regs.csr
.write_field("en", 1);
while (!done) { ... }
}
}
scenario
action xfer_a {
rand bit[16] size;
constraint size in [1..4096];
exec body {
comp.transfer(size);
}
}
realization → operation model
component dma_c {
target function void transfer(bit[16] sz) {
regs.sz.write_val(sz);
regs.csr.write_field("en", 1);
while (!done) { ... }
}
}
calls

## Slide 13: The operation model
The component functions now form a device-programming API we can generate:
PSS operation model
component tree
+ functions (operations)
+ register model
pssc
SystemVerilog classes
UVM sequences, tests
C functions
firmware, emulation, post-si
C++ classes
host models, SystemC
Python module
lab scripts, cocotb
PSS scenarios — call it directly
one source
of truth for
“how to drive
this device”
PSS scenarios still call the same functions directly.

## Slide 14: Bottom line
Single source of truth
PSS gives us device content that can target any language
Pays off immediately
Operation models don't wait for anyone to write PSS tests
Easier PSS adoption
More PSS content available → test scenarios become cheaper later

## Slide 15: Getting technical: operation-model anatomy

## Slide 16: Key requirements
Environment (UVM test · firmware · Python script)
Operation-model instance
State
base addresses, ids, config
Initialization
initialize(base) — bind state
Operations
functions on the component tree,
registers, polling loops
Factory / ctor
create + initialize
returns the API handle
Export API
perform an operation
notify an event (IRQ)
env → model
Import API
memory: read32 / write32
platform: delay, yield, msg
model → env
Your implementation
bus agent / pointer /
fake device
The model holds device knowledge; the environment holds everything else.

## Slide 17: Four things an operation model must provide
Requirement | Purpose | In PSS
Export API | the environment calls in: perform an operation, notify an event | export target function f; on the root
Import API | the model calls out: memory access, platform services | read32/write32, import target function
Initialization | bind state: base addresses, ids | solve function void initialize(...)
State | per-instance data the operations read | component fields, register-group handles
Everything else (scheduling, bus protocol, logging, test intent) stays in the environment.

## Slide 18: SystemVerilog mapping
interface class — EXPORT API
soc_c_ctxt_if
task delay_ticks(int t,
bit[31:0] ticks);
interface class — IMPORT API
soc_c_imp_if
extends pss_mem_if // read32/write32..
task plat_delay_us(int us);
factory + root context
soc_c_root #(Timp)
static function soc_c_ctxt_if
create(Timp imp, addr_handle_t base);
protected soc_c pss_root; // the STATE
protected Timp pss_imp;
your class
my_imp
implements soc_c_imp_if
generated component
soc_c
timer_c tmr[2];
task delay_ticks(...)
implements
implements
implements
owns
calls
create() builds the tree, runs initialize(), returns the export handle.
The handle IS the state — one per device instance.

## Slide 19: SystemVerilog: what you write
class my_imp implements soc_c_imp_if; // IMPORT: you implement
virtual task write32(addr_handle_t addr, bit [31:0] data);
/* start a bus sequence, or call a uvm_reg backdoor ... */
endtask
virtual task read32(addr_handle_t addr, output bit [31:0] data); ... endtask
virtual task plat_delay_us(input int us); #(us * 1us); endtask
endclass
initial begin
my_imp imp = new();
soc_c_ctxt_if soc = soc_c_root#(my_imp)::create(imp, 64'h4000_0000); // FACTORY
soc.delay_ticks(1, 35); // EXPORT
end
Operations are tasks, so they may consume time
One create() per device instance; the returned handle holds the state

## Slide 20: C mapping
State: complete struct types
typedef struct timer_c {
int id;
pssc_addr_t base;
} timer_c;
typedef struct soc_c { timer_c tmr[2]; } soc_c;
Export API + lifecycle
void soc_init(soc_c *_self, pssc_addr_t base);
void soc_delay_ticks(soc_c *_self, int t,
uint32_t ticks);
void timer_start(timer_c *_self, uint32_t ticks);
→ <prefix>_<function>(self, ...)
Import API: model imports
/* named exactly as the model names them */
void plat_delay_us(int us);
/* + pssc_message() if the model reports */
Import API: memory seam (pick one)
--mem-access pointer *(volatile u32*)a
--mem-access functions pssc_mem_read32(a)
--link-style vtable bus->read32(ctx,a)
--lifecycle static no malloc
--addr-bits 32 narrower handles

## Slide 21: C: what you write
#include "soc.h"
/* IMPORT: memory seam (--mem-access functions) */
uint32_t pssc_mem_read32 (pssc_addr_t a) { return *(volatile uint32_t *)a; }
void pssc_mem_write32(pssc_addr_t a, uint32_t d) { *(volatile uint32_t *)a = d; }
/* IMPORT: the model's own imports */
void plat_delay_us(int us) { busy_wait_us(us); }
static soc_c soc; /* STATE: --lifecycle static, no malloc */
int main(void) {
soc_init(&soc, 0x40000000u); /* INIT */
soc_delay_ticks(&soc, 1, 35); /* EXPORT: <prefix>_<function>(self, ...) */
}
Python (op-model-py) and C++ (op-model-cpp) follow the same shape: an import protocol/interface, a root class, and create() or a constructor.

## Slide 22: Lab 1: Core structure
labs/lab1

## Slide 23: Lab 1 goals
Describe an operation model in PSS:
  a component tree holding state
  an initialization function
  operations, exports and imports
Generate it with pssc in four flavors
Integrate it into three environments: C, SystemVerilog, Python
See that all three drive the device identically
C
SystemVerilog
Python
same model · same bus traffic

## Slide 24: The device and the model
Device @ 0x4000_0000
+0x000 timer 0
0x0 CTRL EN, IRQ_EN
0x4 LOAD
0x8 STATUS DONE (W1C)
+0x100 timer 1
0x0 CTRL EN, IRQ_EN
0x4 LOAD
0x8 STATUS DONE (W1C)
soc_c (root)
timer_c tmr[2];
initialize(base)
delay_ticks(t, ticks) export
timer_c
int id; addr_handle_t base;
initialize(i, b)
start(ticks)
is_done() -> bool
wait_done(poll_us)
tmr[0], tmr[1]
plat_pkg
import target function
void plat_delay_us(int us);
calls
write32 / read32 (base + off)
initialize: base + i*0x100
Two timer channels, raw register offsets for now (Lab 2 fixes that).

## Slide 25: PSS: imports (pss/plat_pkg.pss)
// What the operation model needs FROM its environment.
// The environment (UVM test, firmware, Python harness) implements these.
package plat_pkg {
// Wait for (at least) 'us' microseconds of device time.
import target function void plat_delay_us(int us);
}
import target function declares a platform service. The model only names it.
Memory access (read32/write32) is an implicit import, from addr_reg_pkg.
Each generator turns imports into the language's "you implement this" form:
  SV: a method on soc_c_imp_if
  C: an extern prototype
  Py: a method on a Protocol

## Slide 26: PSS: a leaf component (pss/timer_c.pss)
component timer_c {
// --- State: set once at initialization, read by every operation
int id;
addr_handle_t base;
// --- Initialization: bind this instance to its address window
solve function void initialize(int i, addr_handle_t b) {
id = i;
base = b;
}
// --- Operations
target function void start(bit[32] ticks) {
write32(make_handle_from_handle(base, 0x8), 1); // clear DONE
write32(make_handle_from_handle(base, 0x4), ticks); // LOAD
write32(make_handle_from_handle(base, 0x0), 1); // EN
}
target function bool is_done() {
bit[32] sts = read32(make_handle_from_handle(base, 0x8));
return (sts & 1) != 0;
}
target function void wait_done(int poll_us) {
while (!is_done()) { plat_delay_us(poll_us); }
}
}
State
fields every operation reads
Initialization
solve function: binds state once
Operations
target function: touch the device

## Slide 27: PSS: the root (pss/soc_c.pss)
component soc_c {
timer_c tmr[2];
solve function void initialize(addr_handle_t base) {
foreach (tmr[i]) {
tmr[i].initialize(i, make_handle_from_handle(base, i * 0x100));
}
}
// A composite operation: start a timer and block until it expires.
target function void delay_ticks(int t, bit[32] ticks) {
tmr[t].start(ticks);
tmr[t].wait_done(10);
}
// The API the environment sees.
export target function delay_ticks;
}
The root is chosen on the command line (--root soc_c)
Exports select the root functions the environment can call. Sub-component functions remain reachable in C/C++/Py.

## Slide 28: Generating output
PSS sources
plat_pkg.pss
timer_c.pss
soc_c.pss
(dependency order!)
pssc compile
--root soc_c
-t op-model-<flavor>
op-model-sv
soc_c_pkg.sv (+ .svh)
pssc_reg_pkg.sv (runtime core)
op-model-c
soc.h soc.c soc_regs.h
pssc_mem*.h pssc_env.h (runtime core)
op-model-cpp
soc.hpp
pssc_reg.hpp pssc_env.hpp (runtime core)
op-model-py
soc.py
pssc_rt.py (runtime core)
pssc compile pss/plat_pkg.pss pss/timer_c.pss pss/soc_c.pss \
-t op-model-c --root soc_c -o gen/c \
--link-style direct --mem-access functions --lifecycle static

## Slide 29: Available output flavors
-t | Output | Useful options
op-model-sv | package with *_imp_if, *_ctxt_if, *_root | --package NAME
op-model-c | <prefix>.h/.c, private <prefix>_regs.h | --prefix, --link-style, --mem-access, --lifecycle static, --addr-bits 32, --yield import
op-model-cpp | <ns>.hpp, header-only | --namespace, --dispatch {virtual,template}
op-model-py | <module>.py + pssc_rt.py | --py-await {sync,async}
(all) |  | --emit-manifest FILE (JSON: ops, signatures, register offsets), --no-comments
pssc targets lists them all. Each target also tells the model what it can do via target_cfg_pkg (e.g. HAVE_EVENT_WAIT).

## Slide 30: PSS → SystemVerilog
target function bool is_done() {
bit[32] sts = read32(
make_handle_from_handle(base, 0x8));
return (sts & 1) != 0;
}
target function void wait_done(int poll_us) {
while (!is_done()) {
plat_delay_us(poll_us);
}
}
virtual task is_done(output bit status);
bit [31:0] sts;
pss_imp.read32((base + 8), sts);
status = (sts & 1) != 0;
return;
endtask
virtual task wait_done(input int poll_us);
bit pssc_tmp_0;
forever begin
is_done(pssc_tmp_0);
if (!(!(pssc_tmp_0))) break;
pss_imp.plat_delay_us(poll_us);
end
endtask
Return values become an output first argument, since operations are tasks. Address arithmetic is folded: base + 8.

## Slide 31: PSS → C and Python
uint8_t timer_is_done(timer_c *_self) {
uint32_t sts = pssc_r32(pssc_bus(_self),
(_self->base + 8));
return (sts & 1) != 0;
}
void timer_wait_done(timer_c *_self,
int poll_us) {
while (!(timer_is_done(_self))) {
plat_delay_us(poll_us);
}
}
class Timer(object):
def __init__(self, imports: SocImportApi, i, b):
self._imports = imports
self.id = i
self.base = b
def is_done(self):
sts = self._imports.read32((self.base + 8))
return (sts & 1) != 0
def wait_done(self, poll_us):
while not (self.is_done()):
self._imports.plat_delay_us(poll_us)
Comments in the PSS source are carried into every output (--no-comments to drop them).

## Slide 32: What happens at run time
test code
soc_c
tmr[1]
environment (imports)
delay_ticks(1, 35)
start(35)
write32(+0x108, 1)
write32(+0x104, 35)
write32(+0x100, 1)
wait_done(10)
loop while !is_done()
read32(+0x108)
DONE = 0
plat_delay_us(10)
DONE = 1 → return
return

## Slide 33: Environment integration
SystemVerilog
env/sv/tb.sv
class implements soc_c_imp_if
soc_c_root#(T)::create(imp, base)
write32/read32 may consume time
C
env/c/main.c
define pssc_mem_read32/write32
define plat_delay_us
static soc_c soc; soc_init(&soc, base);
Python
env/py/run.py
any object with read32, write32, plat_delay_us
a Protocol: no inheritance needed
Soc(env, base)
All three use a ~40-line fake timer behind the import API, so the lab runs on a laptop.

## Slide 34: Lab 1: run it
cd labs/lab1
make run # gen + run C, SV (Verilator), Python
make run PSSC_SRC=~/projects/psstools/pssc # against a pssc source tree
delay_ticks(1, 35)
[bus] write32 0x40000108 = 0x1
[bus] write32 0x40000104 = 0x23
[bus] write32 0x40000100 = 0x1
done after 4 polls
×3
identical output from C, SV and Python
Same model, same bus traffic.

## Slide 35: Lab 1 exercises
Observe. make gen, then find each PSS element in gen/sv, gen/c, gen/cpp, gen/py: state, initialize, delay_ticks, plat_delay_us, tmr[2]
Add an operation. Give timer_c a stop() (EN=0, clear DONE); add and export soc_c::cancel(int t). Regenerate: where did cancel appear in each flavor?
Change a signature. Give wait_done a max_polls budget and make it return bool; make delay_ticks return it. Update the three harnesses to report a timeout and call cancel()
Solution: labs/lab1/solution, run with make run SOL=1.

## Slide 36: Lab 2: Registers and memory
labs/lab2

## Slide 37: Why a register model?
Lab 1 wrote write32(make_handle_from_handle(base, 0x8), 1).
Offsets
restated by hand; wrong ones fail silently
Fields & masks
positions and masks restated by hand
Access rules
read-only, W1C: invisible in the code
Copies
RTL, UVM RAL, firmware headers each keep their own
PSS 3.x has a register model in addr_reg_pkg. Generate it from the same source as everything else.

## Slide 38: Creating register models
timer.rdl
SystemRDL
(or IP-XACT →
RDL, Rubix…)
peakrdl pss
--pad-tail
timer_regs_pkg.pss
struct ..._s : packed_s<>
(field layout)
component ..._c : reg_c<>
(one register)
component ..._c : reg_group_c
(bank + offsets)
imported by
timer_ch_c.pss
timer_c.pss
pssc →
SV: reg_c #(struct)
C: bitfield unions
Py: _RegValue classes
pssc →
SV: reg_c #(struct)
C: bitfield unions
Py: _RegValue classes
same RDL also feeds
RTL (peakrdl-regblock)
UVM RAL (peakrdl-uvm)
docs (peakrdl-html)
one register spec, many consumers
peakrdl pss rdl/timer.rdl --pad-tail -o pss/timer_regs_pkg.pss

## Slide 39: PSS register-model anatomy
struct timer_ch_regs__ctrl_s : packed_s<LITTLE_ENDIAN>
rsvd_8
31
8
prescale
7
4
rsvd
3
mode
2
irq_en
1
en
0
← field layout
pure component timer_ch_regs__ctrl_c
: reg_c<timer_ch_regs__ctrl_s, READWRITE, 32> {}
read() write(v) write_masked(m, v)
read_val() write_val(raw) write_field("en", 1)
← one register:
value type + access + width
pure component timer_ch_regs_c : reg_group_c
timer_ch_regs__ctrl_c ctrl; // @0x0
timer_ch_regs__load_c load; // @0x4
timer_ch_regs__status_c status; // @0x8
timer_ch_regs__count_c count; // @0xC
get_offset_of_instance("load") → 0x4
← a bank: registers + offsets
In the operation model
component timer_ch_c {
timer_ch_regs_c regs;
init: regs.set_handle(h);
regs.load.write_val(t);
sts = regs.status.read();
if (sts.done == 1) ...
regs.ctrl
.write_field("en", 1);
}

## Slide 40: Generated register package (excerpt)
package timer_regs_pkg {
import addr_reg_pkg::*;
struct timer_ch_regs__status_s : packed_s<LITTLE_ENDIAN> {
bit done; // [0] sw=rw hw=w reset=0x0 dropped: onwrite=woclr
bit busy; // [1] sw=r hw=w reset=0x0
bit[30] rsvd_2; // [31:2] reserved
}
pure component timer_ch_regs__status_c : reg_c<timer_ch_regs__status_s, READWRITE, 32> {}
pure component timer_ch_regs_c : reg_group_c {
timer_ch_regs__ctrl_c ctrl;
timer_ch_regs__load_c load;
timer_ch_regs__status_c status;
timer_ch_regs__count_c count;
pure function bit[64] get_offset_of_instance(string name) {
match (name) { ["ctrl"]: return 0x0; ["load"]: return 0x4; /* ... */ }
}
}
}
onwrite = woclr has no PSS equivalent: peakrdl-pss warns (PSS-W101) and keeps it as a comment.

## Slide 41: Register and memory access functions
Call | On | Bus effect
read() / write(v) | reg_c<R> | one access; value is the packed struct R
read_val() / write_val(raw) | reg_c<R> | one access; raw bit[N]
write_field("en", 1) | reg_c<R> | read-modify-write of one field
write_masked(mask, v) | reg_c<R> | read-modify-write
set_handle(h) | reg_group_c | none: binds the bank to an address (init only)
get_offset_of_instance[_array] | reg_group_c | none: folded to a constant by pssc
read32(h) / write32(h, v), 8/16/64 | addr_handle_t | raw memory access (Lab 1)
make_handle_from_handle(h, off) | addr_handle_t | none: address arithmetic
The field name in write_field is resolved at compile time, so a typo is an error rather than a wrong bit.

## Slide 42: Binding registers to addresses
address map
0x4000_0000
ID
0x4000_0100
ch[0]
CTRL LOAD STATUS COUNT
0x4000_0200
ch[1]
CTRL LOAD STATUS COUNT
timer_c::initialize
solve function void initialize(addr_handle_t base) {
regs.set_handle(base);
foreach (ch[i]) {
ch[i].initialize(i,
make_handle_from_handle(base,
regs.get_offset_of_instance_array("ch", i)));
}
}
Why per-channel components?
• each channel binds its own bank → operations are index-free
• offsets come from the generated group → stated once, in the RDL
• pssc folds the offset to a constant: base + 0x100 + 0x100*i

## Slide 43: The programming sequence (pss/timer_ch_c.pss)
component timer_ch_c {
int id;
timer_ch_regs_c regs; // this channel's register bank
solve function void initialize(int i, addr_handle_t bank) {
id = i;
regs.set_handle(bank);
}
target function void configure(timer_cfg_s cfg) {
timer_ch_regs__ctrl_s ctrl;
timer_ch_regs__load_s load;
load.value = cfg.ticks;
regs.load.write(load);
ctrl.en = 0; ctrl.irq_en = cfg.irq_en; // build the value,
ctrl.mode = cfg.periodic; ctrl.prescale = cfg.prescale;
regs.ctrl.write(ctrl); // then write it once
}
target function void start() {
regs.status.write_val(1); // DONE is write-1-to-clear
regs.ctrl.write_field("en", 1); // read-modify-write of one field
}
target function bool is_done() {
timer_ch_regs__status_s sts = regs.status.read();
return sts.done == 1;
}
}

## Slide 44: Register-operation details
What reaches the bus
regs.load.write(v)
W
LOAD = v
whole register, one write
regs.load.write_val(0x19)
W
LOAD = 0x19
raw value, one write
regs.status.read()
R
STATUS
one read → struct
regs.ctrl.write_field("en", 1)
R
CTRL
W
CTRL | en
read-modify-write (LRM §21.14.1)
regs.ctrl.write_masked(m, v)
R
CTRL
W
(cur&~m)|(v&m)
read-modify-write
A field write still READS the register. If a read has side effects (clear-on-read), that matters.

## Slide 45: Register-operation pitfalls
Field writes read first
write_field/write_masked are a read-modify-write (PSS 3.1 §21.14.1). On a register with clear-on-read bits, that read is a side effect.
W1C registers
Write the clear value with write_val. Don't RMW a W1C register, or you'll clear bits you didn't mean to.
Whole vs. field writes
Build a struct and write() once when configuring. Use write_field() to flip one bit of live state.
Reserved bits
Use --pad-tail so every struct spans the full register width. Otherwise C gets a uint8_t raw for a 32-bit register.
Device semantics
W1C, RC and sticky bits aren't in the PSS type. Document them in the operation, where the next reader will look.

## Slide 46: What it generates
// SV: reg_c parameterized by the packed struct
class timer_ch_regs_c;
reg_c #(timer_ch_regs__ctrl_s) ctrl;
reg_c #(timer_ch_regs__load_s) load;
reg_c #(timer_ch_regs__status_s) status;
reg_c #(timer_ch_regs__count_s,
READONLY) count;
...
endclass
virtual task start();
regs.status.write_val(1);
regs.ctrl.write_field(
TIMER_CH_REGS__CTRL_en, 1);
endtask
/* C: bitfield unions, private header */
typedef union { uint32_t raw; struct {
uint32_t en : 1;
uint32_t irq_en : 1;
uint32_t mode : 1;
uint32_t rsvd_3 : 1;
uint32_t prescale : 4;
uint32_t rsvd_8 : 24;
}; } timer_ch_regs__ctrl_s;
void timer_ch_start(timer_ch_c *_self) {
timer_ch_regs_status_write_val(_self, 1);
timer_ch_regs_ctrl_write_masked(
_self, 1, 1);
}

## Slide 47: Lab 2: run it
cd labs/lab2
make regs # SystemRDL -> pss/timer_regs_pkg.pss (checked in; needs peakrdl-pss)
make run
one_shot(0, 25) — identical in C, SystemVerilog and Python
W
ch0.LOAD = 0x19
configure: load.write()
W
ch0.CTRL = 0x00
configure: ctrl.write() (EN=0)
W
ch0.STATUS = 0x01
start: clear DONE (W1C)
R
ch0.CTRL -> 0x00
start: write_field("en",1) — read…
W
ch0.CTRL = 0x01
…modify, write
R
ch0.STATUS -> 0x02
wait_done: BUSY
R
ch0.STATUS -> 0x02
(plat_delay_us between polls)
R
ch0.STATUS -> 0x02
R
ch0.STATUS -> 0x01
DONE → return

## Slide 48: Lab 2 exercises
Change the register spec. Add an ovf bit to STATUS in rdl/timer.rdl (bit 2, W1C: "expired again while DONE was set"). make regs gen and find ovf in every flavor. You edited no PSS.
Write a programming sequence. Add timer_ch_c::ack() (read STATUS, clear DONE|OVF, return ovf) and timer_c::periodic(int c, bit[32] ticks, int n) → number of missed expiries. Export it.
Explain the trace. Run periodic(1, 20, 3) and periodic(1, 4, 2). Why does the second miss expiries? Which bus accesses come from write_field?
Solution: labs/lab2/solution, run with make run SOL=1.

## Slide 49: Wrap-up
An operation model is PSS's device knowledge, separated from scenarios
Four parts: export API, import API, initialization, state
pssc turns one model into SV, C, C++ and Python, each idiomatic for its users
Register models come from the register spec (SystemRDL → peakrdl pss)
Today: every team runs the same programming sequence. Later: PSS tests reuse the same functions.